## Slide 1: Combined Effects of Fast-Velocity Weakening Friction and Stress Heterogeneity Control Megathrust Earthquake Re-Activation, High-Frequency Radiation, and Arrest in 3D Dynamic Rupture Simulations of the 2011 Mw 9.0 Tohoku-Oki Earthquake
NMEM 2024
Jeremy Wing Ching Wong, Alice-Agnes Gabriel, Wenyuan Fan
3D dynamic rupture simulation of the 2011 Tohoku-Oki earthquake rupture featuring spontaneous re-activation, high-frequency radiation, and arrest
8s
15s
Rupture front
Re-nucleation
25s
35s
50s
60s
Re-nucleation
Down-dip slip pulses
Rupture front

## Slide 2
Rupture re-activation during the Tohoku-Oki earthquake
Lee et al., 2011
Finite-fault model using regional seismic data
Strong-ground motions records
Strong ground motion recordings and finite-fault inversions suggest rupture re-activation at the hypocenter region of the Tohoku-Oki earthquake
First wavefront
Second wavefront
Notes: Just in case there are questions - there is a more faint 3rd pulse also visible in the data and finite fault model

## Slide 3
Rupture re-activation during the Tohoku-Oki earthquake
Lee et al., 2011
Finite-fault model using regional seismic data
Strong-ground motions records
Strong ground motion recordings and finite-fault inversions suggest rupture re-activation at the hypocenter region of the Tohoku-Oki earthquake
First wavefront
Second wavefront
Notes: The first rupture caused updip
While the second rupture caused on extension of the rupture both up dip and down-dip direction
Episodic rupture fronts at the end of the third rupture

## Slide 4: Down-dip high-frequency radiation
Lay et al., 2012
Teleseismic back-projection analysis suggest down-dip high-frequency radiation
Large fault displacements occurred at shallow depths
Notes: teleseismic short-period radiation preferentially emanated from the deeper portion of the megathrusts whereas the largest fault displacements occurred at shallower depths but produced relatively little coherent short-period radiation

## Slide 5
Along-strike rupture arrest and slip to the trench
Shibazaki et al., 2019
Tohoku-Oki earthquake did not rupture the entire megathrust
Large slip towards the trench is observed
Ueda et al., 2023
Near trench bathymetric changes before and after Tohoku-Oki earthquake

## Slide 6
We propose a self-consistent way to reproduce a realistic Tohoku-Oki earthquake rupture with the observed complexity
rupture re-activation
down-dip high frequency radiation
spontaneous rupture arrest
large slip towards the trench
Friction or Stress - What governs megathrust earthquake complexity?
Stress asperities?
Frictional asperities and barriers?
Complex dynamic friction evolution?
Ma 2023
Galvez et al., 2020
Notes: Stress asperites refers to area with large stress drop while frictional barriers refers to area with a large strength excess than their surroundings difference between 'barrier' and 'asperity' : large stress-drop regions (“asperities”) vs areas with a larger strength excess than their surroundings (“barriers”)

## Slide 7: 3D model with realistic slab geometry and topography
Realistic slab geometry from Japan Integrated Velocity Structure Model (Koketsu, et al. 2012)
3D Topography and bathymetry (GEBCO)
1D elastic layers Fukuyama (1998)
Unstructured tetrahedral mesh (10,643,928 elements) Velocity aware meshing to resolve wave frequencies up to 0.5 Hz
Depth dependent effective normal stress (overburden stress from 1D velocity layers + constant fluid pressure ratio γ = 0.9 )

## Slide 8
Velocity weakening | Velocity strengthening
Downdip limit (50km)
Seismogenic zone
Updip limit (9km)
Updip limit (10km) from JIVSM model as boundary between accretionary wedge and crustal bedrock
Downdip limit (50km) from the seismicity of the Japan trench subduction zone (Nishikawa, et al., 2023)
Fast velocity-weakening rate-and-state friction
Proxy to flash-heating that weakens friction at high slip-rate (Vw = 0.1 m/s)
Tohoku-Oki earthquake rupture extent
Trench
Nielsen and Madariaga, 2003

## Slide 9: Stress heterogeneity
Regional stress model
(depth dependent, constrained from World Stress Map, Heidbach et al., 2016)
Finite-fault model informed multi-scale stress heterogeneity
-30 30
Along-dip traction [MPa]
Median slip model based on 32 existent inversions Wong et al., submitted
Yagi et al., 2011
Kubota et al., 2023

## Slide 10: Complex rupture evolution and re-activation
Only stress heterogeneity is introduced into the simulation
Rupture re-activates in hypocenter region and generates down-dip slip pulses
Rupture re-activation
median finite-fault model informed multi-scale stress heterogeneity
complex slip rate evolution with rupture reactivation and down-dip slip pulses
smooth final slip distribution
complex peak slip rate distribution
Notes: Mg1_RSs1_NUC_R1.5_S10_R001_sl1_t120s_OP09
Compare difference between Mg1_RS1_NUC

## Slide 11: Complex rupture evolution and re-activation
Only stress heterogeneity is introduced into the simulation
Rupture re-activates in hypocenter region and generates down-dip slip pulses
Rupture re-activation
median finite-fault model informed multi-scale stress heterogeneity
complex slip rate evolution with rupture reactivation and down-dip slip pulses
smooth final slip distribution
complex peak slip rate distribution
Notes: Mg1_RSs1_NUC_R1.5_S10_R001_sl1_t120s_OP09
Compare difference between Mg1_RS1_NUC

## Slide 12: Episodic re-activation at the hypocenter due to strong frictional restrengthening
Up-dip
Down-dip
Strong coseismic restrengthening re-activates rupture in the hypocenter region
down-dip slip pulses
re-activation
Notes: M_RSs1_NUC_Tn36_R1.2_S10_R001_sl0.5_t120s_OP09_srW0.1-fault.xdmf

## Slide 13: Episodic re-activation at the hypocenter due to strong frictional restrengthening
Along dip profile of slip-rate and traction
Hypocenter slip-rate and traction evolution
Stress drop
Coseismic restrengthening
Rupture episodes: 1 2 3 4 5
Strong coseismic restrengthening re-activates rupture in the hypocenter region
Up-dip
Down-dip
Notes: M_RSs1_NUC_Tn36_R1.2_S10_R001_sl0.5_t120s_OP09_srW0.1-fault.xdmf
growing stress concentration left behind an initial self-similar slip pulse

## Slide 14: Synthetic waveforms on rupture reactivation
E-W component surface velocity
Slip rate
Final slip distribution

## Slide 15: Synthetic waveforms on rupture reactivation
Final slip distribution

## Slide 16: Does stress-heterogeneity play a role in rupture reactivation and down-dip slip pulses?
-30 30
Along-dip traction [MPa]
Median slip model based on 32 existent inversions, Wong et al., submitted
Regional stress model
(depth dependent, constrained from World Stress Map, Heidbach et al., 2016)
Finite-fault model informed stress heterogeneity

## Slide 17: Regional-stress model - no stress heterogeneity
Strong coseismic restrengthening reactivates rupture in the hypocenter region and down-dip slip pulses
t = 11s re-nucleate at the hypocenter
t = 57s secondary downdip rupture front
t = 77s delayed pulses at downdip region
t = 40s rupture limited at downdip and free-surface reflection
Along-dip traction Slip-rate

## Slide 18: Regional-stress model - no stress heterogeneity
Strong coseismic restrengthening reactivates rupture in the hypocenter region and down-dip slip pulses
t = 11s re-nucleate at the hypocenter
t = 57s secondary downdip rupture front
t = 77s delayed pulses at downdip region
t = 40s rupture limited at downdip and free-surface reflection
Along-dip traction Slip-rate

## Slide 19: Regional-stress model - no stress heterogeneity
Strong coseismic restrengthening reactivates rupture in the hypocenter region and down-dip slip pulses
t = 11s re-nucleate at the hypocenter
t = 57s secondary downdip rupture front
t = 77s delayed pulses at downdip region
t = 40s rupture limited at downdip and free-surface reflection
Along-dip traction Slip-rate

## Slide 20: Regional-stress model - no stress heterogeneity
Strong coseismic restrengthening reactivates rupture in the hypocenter region and down-dip slip pulses
t = 11s re-nucleate at the hypocenter
t = 57s secondary downdip rupture front
t = 77s delayed pulses at downdip region
t = 40s rupture limited at downdip and free-surface reflection
Along-dip traction Slip-rate
Notes: Early healing generated by barrier? Hence leading the coseismic restrengthening at down dip region, leading to the slip pulses at depth

## Slide 21: Does stress-heterogeneity play a role in rupture reactivation?
Coseismic restrengthening
stress drop
Stress heterogeneity is not required for rupture reactivation and down-dip pulses
Strong coseismic re-strengthening leads to rupture reactivation and down-dip pulses
Along dip profile of slip-rate and traction
Hypocenter slip-rate and traction evolution
Notes: RegStr06_RSs1_NUC_R1.2_S05_sl0.8_t200s-fault.xdmf

## Slide 22: Spontaneous rupture arrest due to stress heterogeneity
Spontaneous rupture arrest along-strike due to stress heterogeneity
Slip [m]
-30 30
Along-dip traction [MPa]
-30MPa 30 MPa
Along-dip traction [MPa]
Resulting slip distribution
Median finite-fault model informed multi-scale stress heterogeneity
Regional initial stress (depth-dependent)
Resulting slip distribution
Notes: Mg1_RSs1_NUC_R1.5_S10_R001_sl1_t120s_OP09
Compare difference between Mg1_RS1_NUC

## Slide 23: Spontaneous rupture arrest due to stress heterogeneity
Spontaneous rupture arrest along-strike due to stress heterogeneity
Slip [m]
-30 30
Along-dip traction [MPa]
-30MPa 30 MPa
Along-dip traction [MPa]
Resulting slip distribution
Median of 32 kinematic slip model
Median finite-fault model informed multi-scale stress heterogeneity
Regional initial stress (depth-dependent)
Resulting slip distribution
Notes: Mg1_RSs1_NUC_R1.5_S10_R001_sl1_t120s_OP09
Compare difference between Mg1_RS1_NUC

## Slide 24: Conclusions - What governs the 3D complexity of the Tohoku-Oki earthquake?
Coseismic re-strengthening controls rupture reactivation and down-dip slip pulses
Stress heterogeneity is not required for rupture reactivation or down-dip slip pulses
Stress heterogeneity informed by finite-fault models is sufficient to spontaneously arrest earthquake rupture along-strike